## Slide 1: Calibration Challenges
Kevin Bandura
West Virginia University

## Slide 2: Foregrounds
Foregrounds
21cm signal
Shaw et al. 2015

## Slide 3: Foregrounds
Filtered Foregrounds
Filtered
21cm signal
Shaw et al. 2015
Error in Power spectrum due to % error in gain

## Slide 4: Requirements
Beam Calibration to better than 0.1%
Complex Gain target better than 1% (Shaw et al. 2015)
  ~0.3% amplitude
  ~0.003 Radian phase
Redundant Baseline compression or FFT Beamforming will require Real-time Calibration

## Slide 5: Redundant Baseline Calibration
Requires baselines to be actually redundant.
Corr-cal
  Imperfect Sky model + nearly redundant baselines

## Slide 6: Analog System
Notes: The chime analog system is a simple design. There is no mixing, we directly amplify the signal. On the focal-line there is the feed and LNA, the signal is then transmitted over coax, to a Shielded container. There the signal is filtered and further amplified to a level which can be digitized by the adc.

## Slide 7: Temperature Stability
Current analog amplifier chains have
~0.2 % / °C amplitude variation
Maintain to 1°C
  Measure and model temperature to remove more variation
Analog chain phase
  Cable lengths change ~10-50ppm/ °C ~20ppm/ °C LMR400
    100m cable -> 1-5mm cable change per °C
    0.002-0.01 radians/ °C per cable.
  Fiber similar, ~10ppm/ °C.
  Steel ~15 ppm / °C
Maintain Entire Analog System to within ~1 °C

## Slide 8: Measure Gain Variations
Credit: Seth Siegel
Amplitude
Ambient
Temperature °C

## Slide 9
Thermal Model to remove common mode amplitude fluctuations. Approaching the ~0.5% amplitude stability
TauA
17 Transits
VirA
17 Transits
CHIME Pathfinder Temperature Stability
Common Mode
Fractional Amplitude Fluctuations
Tsource - Tcal [°C]
Credit: Seth Siegel

## Slide 10: Add Temperature Stabilization
Heater and/or TEC:
  Maintain ~ 20-40°C
Digital electronics at focus
Measure each amplifier and transmission system

## Slide 11: Broadband Signal Injection
Broadband Injected Signal
Measured by Correlator
Notes: For gain calibration using a broadband injected signal. The signal is injected into the feeds with an antenna, and also measured directly into the correlator. We have tested this system as shown with 8 channels on the pathfinder. We were able to solve for the relative gains to better than 1% on second timescales.

## Slide 12: Gain Calibration Visibilities

## Slide 13: Broadband Signal Injection

## Slide 14: Broadband Signal Injection
Credit: Juan Mena
Calibration to the 1% level.
Injection system must be stable and uniform

## Slide 15: Pulse Injection
Instead of broadband noise, inject < ns pulse
Measure in time domain.
“Strong Signal”, synchronize and blank out
Bandpass Calibration. (Patra et. al. 2017)
Patra et. al. 2017
Patra et. al. 2017

## Slide 16: Beam Calibration
X
Transiting
source
Holography

## Slide 17: Holography
Berger et al 2016

## Slide 18: Drone Calibration

## Slide 19: Improved Calibration Source

## Slide 20: Summary
Need to understand Gain to ~1% and Beams to 0.1%
Measure parameters correlated with Gain variation
Measure gain variation with sky and synthetic sources
Measure Beam with holography
Measure Beam with drones

## Slide 21: Correlator F-Engine and Networking

## Slide 22: Correlator F-Engine
Two FMC Mezzanines
FPGA
Two Gbit
Ethernet
Digital signals come in/out the back
ARM processor
DDR RAM
Ethernet
9U VME Front-panel
Custom Backplane
Power, clock, timestamp
Board inter-connect

## Slide 23: Correlator –X Engine GPU
Pathfinder: 13T complex MAC/s
CHIME: 840 TcMAC/s
AMD s9300x2
FRB FFT Beamformer
Pulsar Beamformer

## Slide 24: CHIME
The Canadian Hydrogen Intensity Mapping Experiment
Drift scan = 1/2 sky daily
  Due to actual N-S beam
400-800MHz band
  0.8 < z < 2.5 (for 21cm)
390kHz frequency resolution
  24kHz (16x) for FRB
13’-26’ spatial resolution
  (5-10 min observing time)
BAO scale to <10%
  w0 to ±0.05 (w0 ~ 1)
  wa to ±0.2 (wa ~ 0)

## Slide 25: HIRAX
1024 6m Dishes
Karoo Desert
South Africa

## Slide 26: Broadband Signal Injection